## Slide 1: Introduction to ARM processor

## Slide 2: Intro..
ARM founded in November 1990
  Advanced RISC Machines
Company headquarters in Cambridge, UK
  Processor design centers in Cambridge, Austin, and Sophia Antipolis
  Sales, support, and engineering offices all over the world
Best known for its range of RISC processor cores designs
  Other products – fabric IP, software tools, models, cell libraries - to help partners develop and ship ARM-based SoCs
ARM does not manufacture silicon
  http://www.arm.com/aboutarm/

## Slide 3: Intro…
1985: Acorn Computer Group manufactures the first commercial RISC microprocessor.
1990: Acorn and Apple participation leads to the founding of Advanced RISC Machines (A.R.M.).
1991: ARM6, First embeddable RISC microprocessor.
1992 – 1994: Various companies use ARM (Sharp, Samsung), while in 1993 ARM7, the first multimedia microprocessor is introduced.

## Slide 4: Intro…
1995: Introduction of Thumb and ARM8.
1996 – 2000: Alcatel, Huindai, Philips, Sony, use ΑRM, while in 1999 η ARM cooperates with Erickson for the development of Bluetooth.
2000 – 2002: ARM’s share of the 32 – bit embedded RISC microprocessor market is 80%. ARM Developer Suite is introduced.

## Slide 5: Features
Architectural simplicity which allows very small implementations resulting in Load – store architecture
32 bit data bus
3 addressing modes
    High performance
    Low code size
    Low power consumption
    Low silicon area
    Single cycle execution
Pipeline Organization

## Slide 6: ARM Architecture 3 stage pipelining

## Slide 7: 3 stage piplelining
cycle
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
instruction
t
t+1
t+2
t+3
t+4
i
i+1
i+2

## Slide 8: Operating modes
The ARM has seven basic operating modes:
  User : unprivileged mode under which most tasks run
  FIQ : entered when a high priority (fast) interrupt is raised
  IRQ : entered when a low priority (normal) interrupt is raised
  Supervisor : entered on reset and when a Software Interrupt instruction is executed
  Abort : used to handle memory access violations
  Undef : used to handle undefined instructions
  System : privileged mode using the same registers as user mode
Notes: The Programmers Model can be split into two elements - first of all, the processor modes and secondly, the processor registers. So let’s start by looking at the modes.
Now the typical application will run in an unprivileged mode know as “User” mode, whereas the various exception types will be dealt with in one of the privileged modes : Fast Interrupt, Supervisor, Abort, Normal Interrupt and Undefined (and we will look at what causes each of the exceptions later on).
NB - spell out the word FIQ, otherwise you are saying something rude in German!
One question here is what is the difference between the privileged and unprivileged modes? Well in reality very little really - the ARM core has an output signal (nTRANS on ARM7TDMI, InTRANS, DnTRANS on 9, or encoded as part of HPROT or BPROT in AMBA) which indicates whether the current mode is privileged or unprivileged, and this can be used, for instance, by a memory controller to only allow IO access in a privileged mode. In addition some operations are only permitted in a privileged mode, such as directly changing the mode and enabling of interrupts.
All current ARM cores implement system mode (added in architecture v4). This is simply a privileged version of user mode. Important for re-entrant exceptions because no exceptions can cause system mode to be entered.

## Slide 9: Registers
ARM has 37 registers all of which are 32-bits long.
  1 dedicated program counter
  1 dedicated current program status register
  5 dedicated saved program status registers
  30 general purpose registers
The current processor mode governs which of several banks is accessible. Each mode can access
  a particular set of r0-r12 registers
  a particular r13 (the stack pointer, sp) and r14 (the link register, lr)
  the program counter, r15 (pc)
  the current program status register, cpsr
Privileged modes (except System) can also access
  a particular spsr (saved program status register)

## Slide 10: ARM Programming Model
r13_und
r14_und
r14_irq
r13_irq
SPSR_und
r14_abt
r14_svc
user mode
fiq
mode
svc
mode
abort
mode
irq
mode
undefi
ned
mode
usable in user mode
system modes only
r13_abt
r13_svc
r8_fiq
r9_fiq
r10_fiq
r1
1_fiq
SPSR_irq
SPSR_abt
SPSR_svc
SPSR_fiq
CPSR
r14_fiq
r13_fiq
r12_fiq
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r1
1
r12
r13
r14
r15 (PC)
Notes: Abort mode: Όταν απέτυχε η προσπάθεια να γίνει πρόσβαση σε μνήμη
Supervisor mode: Αμέσως μετά το reset, λειτουργικό σύστημα kernel
System mode: Special user mode, full access to cpsr
Undefined mode: When undefined instruction, or instruction not supported by implementation

## Slide 11: Program Status Registers
Condition code flags
  N = Negative result from ALU
  Z = Zero result from ALU
  C = ALU operation Carried out
  V = ALU operation oVerflowed
Interrupt Disable bits.
  I = 1: Disables the IRQ.
  F = 1: Disables the FIQ.
T Bit
  Architecture xT only
  T = 0: Processor in ARM state
  T = 1: Processor in Thumb state
Mode bits
  Specify the processor mode