## Slide 1: ADVANCED PROCESSORS & CONTROLLERS
Module 6

## Slide 2: Contents
Advanced Microprocessor Architecture- Pentium
Concept of CISC and RISC processors
Introduction to ARM processor and PIC micro controller

## Slide 4: Pentium Family
Intel introduced microprocessors in 1969
  4-bit microprocessor 4004
  8-bit microprocessors
    8080
    8085
  16-bit processors
    8086 introduced in 1979
      20-bit address bus, 16-bit data bus
    8088 is a less expensive version
      Uses 8-bit data bus
    Can address up to 4 segments of 64 KB
    Referred to as the real mode
  80186
    A faster version of 8086
    16-bit data bus and 20-bit address bus
    Improved instruction set
  80286 was introduced in 1982
    24-bit address bus
    16 MB address space
    Enhanced with memory protection capabilities
    Introduced protected mode
      Segmentation in protected mode is different from the real mode
    Backwards compatible

## Slide 5: Pentium Family
  80386 was introduced 1985
    First 32-bit processor
    32-bit data bus and 32-bit address bus
    4 GB address space
    Segmentation can be turned off (flat model)
    Introduced paging
  80486 was introduced 1989
    Improved version of 386
    Combined coprocessor functions for performing floating-point arithmetic
    Added parallel execution capability to instruction decode and execution units
      Achieves scalar execution of 1 instruction/clock
    Later versions introduced energy savings for laptops
  Pentium (80586) was introduced in 1993
    Similar to 486 but with 64-bit data bus
    Wider internal data paths
      128- and 256-bit wide
    Added second execution pipeline
      Superscalar performance
      Two instructions/clock
    Doubled on-chip L1 cache
      8 KB data
      8 KB instruction
    Added branch prediction

## Slide 6: Pentium Family
  Pentium Pro was introduced in 1995
    Three-way superscalar
      3 instructions/clock
    36-bit address bus
      64 GB address space
    Introduced dynamic execution
      Out-of-order execution
      Speculative execution
    In addition to the L1 cache
      Has 256 KB L2 cache
  Pentium II was introduced in 1997
    Introduced multimedia (MMX) instructions
    Doubled on-chip L1 cache
      16 KB data
      16 KB instruction
    Introduced comprehensive power management features
      Sleep
      Deep sleep
    In addition to the L1 cache
      Has 256 KB L2 cache
  Pentium III, Pentium IV,…
For more information visit https://en.wikipedia.org/wiki/List_of_Intel_microprocessors

## Slide 7: Pentium Processor

## Slide 8: Pentium Processor
Data bus (D0 – D 63)
  64-bit data bus
Address bus (A3 – A31)
  Only 29 lines
    No A0-A2 (due to 8-byte wide data bus)
Byte enable (BE0# - BE7#)
  Identifies the set of bytes to read or write
    BE0# : least significant byte (D0 – D7)
    BE1# : next byte (D8 – D15)
    …
    BE7# : most significant byte (D56 – D63)
  Any combination of bytes can be specified
Data parity (DP0 – DP7)
  Even parity for 8 bytes of data
    DP0 : D0 – D7
    DP1 : D8 – D15
    …
    DP7 : D56 – D63
Parity check (PCHK#)
    Indicates the parity check result on data read
    Parity is checked only for valid bytes
    Indicated by BE# signals

## Slide 9: Pentium Processor
Parity enable (PEN#)
  Determines whether parity check should be used
Address parity (AP)
  Bad address parity during inquire cycles
Memory/IO (M/IO#)
  Defines bus cycle: memory or I/O
Write/Read (W/R#)
  Distinguishes between write and read cycles
Data/Code (D/C#)
  Distinguishes between data and code
Cacheability (CACHE#)
  Read cycle: indicates internal cacheability
  Write cycle: burst write-back
Bus lock (LOCK#)
  Used in read-modify-write cycle
  Useful in implementing semaphores
Interrupt (INTR)
  External interrupt signal
Nonmaskable interrupt (NMI)
  External NMI signal

## Slide 10: Pentium Processor
Clock (CLK)
  System clock signal
Bus ready (BRDY#)
  Used to extend the bus cycle
    Introduces wait states
Bus request (BREQ)
  Used in bus arbitration
Backoff (BOFF#)
  Aborts all pending bus cycles and floats the bus
  Useful to resolve deadlock between two bus masters
Bus hold (HOLD)
  Completes outstanding bus cycles and floats bus
  Asserts HLDA to give control of bus to another master
Bus hold acknowledge (HLDA)
  Indicates the Pentium has given control to another local master
  Pentium continues execution from its internal caches
Cache enable (KEN#)
  If asserted, the current cycle is transformed into cache line fill

## Slide 11: Pentium Processor
Write-back/Write-through (WB/WT#)
  Determines the cache write policy to be used
Reset (RESET)
  Resets the processor
  Starts execution at FFFFFFF0H
  Invalidates all internal caches
Initialization (INIT)
  Similar to RESET but internal caches and FP registers are not flushed
  After powerup, use RESET (not INIT)
Notes: a semaphore is a variable or abstract data type that is used for controlling access, by multiple processes, to a common resource in a concurrent system such as a multiprogramming operating system.

## Slide 12: Pentium Architecture
Notes: A translation lookaside buffer (TLB) is a memory cache that stores recent translations of virtual memory to physical addresses for faster retrieval.

## Slide 13: Features
Superscalar Execution
  the Pentium processor can sometimes execute two instructions simultaneously.
Pipeline Architecture:
  the Pentium processor executes instructions in five stages.
  This staging, or pipelining, allows the processor to overlap multiple instructions so that it takes less time to execute two instructions in a row.
  Because of its superscalar architecture, the Pentium processor has two independent processor pipelines.

## Slide 14: Pipeline concept
Pre fetch Instruction
Decode Instruction and generate control word
Generate control word and data memory address
Address data cache
Calculate ALU result
Write back results
Generate control word and data memory address
Address data cache
Calculate ALU result
Write back results
U pipe
V pipe

## Slide 15: Features
Branch Target Buffer:
  It fetches the branch target instruction before it executes the branch instruction.
Dual 8-KB On-Chip Caches:
  Has two separate 8-kilobyte (KB) caches on chip
    one for instructions and
    one for data
  --which allows the Pentium processor to fetch data and instructions from the cache simultaneously.
Write-Back Cache:
  When data is modified; only the data in the cache is changed.
  Memory data is changed only when the Pentium processor replaces the modified data in the cache with a different set of data

## Slide 16: Features
64-Bit Bus
  Can handle up to twice the data load of the Intel486 processor at the same clock frequency.
Instruction Optimization:
  Has been optimized to run critical instructions in fewer clock cycles than the Intel486 processor.
Floating-Point Optimization:
  Executes individual instructions faster through execution pipelining, which allows multiple floating-point instructions to be executed at the same time.

## Slide 17: Pentium Registers

## Slide 18: Flag Register

## Slide 19: Pentium Registers
Control registers
  (E)IP
    Program counter
  (E) FLAGS
    Status flags
      Record status information about the result of the last arithmetic/logical instruction
    Direction flag
      Forward/backward direction for data copy
    System flags
      IF : interrupt enable
      TF : Trap flag (useful in single-stepping)

## Slide 20: Pentium Registers
Segment register
  Six 16-bit registers
  Support segmented memory architecture
  At any time, only six segments are accessible
  Segments contain distinct contents
    Code
    Data
    Stack
    Extra

## Slide 21: Real Mode Architecture
Pentium supports two modes
  Real mode
    Uses 16-bit addresses
    Runs 8086 programs
    Pentium acts as a faster 8086
  Protected mode
    32-bit mode
    Native mode of Pentium
    Supports segmentation and paging

## Slide 22: Real Mode Architecture (cont’d)
Segmented organization
  16-bit wide segments
  Two components
    Base (16 bits)
    Offset (16 bits)
Two-component specification is called logical address
  Also called effective address
20-bit physical address

## Slide 23: Real Mode Architecture (cont’d)
Programs can access up to six segments at any time
Two of these are for
  Data
  Code
Another segment is typically used for
  Stack
Other segments can be used for
  data, code,..

## Slide 24: Protected Mode Architecture
Supports sophisticated segmentation
Segment unit translates 32-bit logical address to 32-bit linear address
Paging unit translates 32-bit linear address to 32-bit physical address
  If no paging is used
    Linear address = physical address

## Slide 25: Protected Mode Architecture (cont’d)
Address translation

## Slide 26: Protected Mode Architecture (cont’d)
Index
  Selects a descriptor from one of two descriptor tables
    Local
    Global
Table Indicator (TI)
  Select the descriptor table to be used
    0 = Local descriptor table
    1 = Global descriptor table
Requestor Privilege Level (RPL)
  Privilege level to provide protected access to data
    Smaller the RPL, higher the privilege level

## Slide 27: Protected Mode Architecture (cont’d)
  Visible part
    Instructions to load segment selector
        mov, pop, lds, les, lss, lgs, lfs
  Invisible
    Automatically loaded when the visible part is loaded from a descriptor table

## Slide 28: Protected Mode Architecture (cont’d)
Segment descriptor

## Slide 29: Protected Mode Architecture (cont’d)
Base address
  32-bit segment starting address
Granularity (G)
  Indicates whether the segment size is in
    0 = bytes, or
    1 = 4KB
Segment Limit
  20-bit value specifies the segment size
    G = 0: 1byte to 1 MB
    G = 1: 4KB to 4GB, in increments of 4KB
D/B bit
  Code segment
    D bit: default size operands and offset value
      D = 0: 16-bit values
      D = 1: 32-bit values
  Data segment
    B bit: controls the size of the stack and stack pointer
      B = 0: SP is used with an upper bound of FFFFH
      B = 1: ESP is used with an upper bound of FFFFFFFFH
  Cleared for real mode
  Set for protected mode

## Slide 30: Protected Mode Architecture (cont’d)
S bit
  Identifies whether
    System segment, or
    Application segment
Descriptor privilege level (DPL)
  Defines segment privilege level
Type
  Identifies type of segment
    Data segment: read-only, read-write, …
    Code segment: execute-only, execute/read-only, …
P bit
  Indicates whether the segment is present
Three types of segment descriptor tables
  Global descriptor table (GDT)
    Only one in the system
    Contains OS code and data
    Available to all tasks
  Local descriptor table (LDT)
    Several LDTs
    Contains descriptors of a program
  Interrupt descriptor table (IDT)
    Used in interrupt processing

## Slide 31: Protected Mode Architecture (cont’d)
Segmentation Models
  Pentium can turn off segmentation
  Flat model
    Consists of one segment of 4GB
    E.g. used by UNIX
  Multisegment model
    Up to six active segments
    Can have more than six segments
      Descriptors must be in the descriptor table
    A segment becomes active by loading its descriptor into one of the segment registers

## Slide 32: Protected Mode Architecture (cont’d)

## Slide 33: Default Segments
Pentium uses default segments depending on the purpose of the memory reference
  Instruction fetch
    CS register
  Stack operations
    16-bit mode: SP
    32-bit mode: ESP
  Accessing data
    DS register
    Offset depends on the addressing mode

## Slide 34: Concept of CISC and RISC
Aspect | RISC | CISC
Acronym | Reduced Instruction Set Computer | Complex Instruction Set Computer
Instruction set | Reduced | Complex
Compiler design | Easy to design | Hard to design
Hardware/Software | Stresses more on software | Stresses more on hardware
Memory management | Memory-to-memory operations | Register-to-register operations
Code size | High in code size | Less in code size
Clocking | Single clock is used | Multiple clocks are used
Instruction length | Single word instruction | Variable length instruction
Pipelining | Pipelining is the major feature | Doesn’t support pipelining

## Slide 36: Guess….